## Slide 1: RAP N°2
MAI 2021
CÉDRIC LEFEBVRE et YESID BELLO
BASTIEN, CLEMENT et HUGO
Notes: (20s)

## Slide 2: NAVeco system.
Environment
(Traffic, Topography, …)
Destination
Arrival time
Nav. parameters
Segmentation
Optimization
Constraints
parameters
Vehicle
(ACC, …)
Phone, …
or
Feedback
Speed reference
Vehicle
(Mass, SCx, …)
Position reference (itinerary)
Dynamic model
(x, v, e)
Segmentation
Optimization
(Electrical)
Optimization(thermal)
NAVeco presentation
Notes: (1min30)

## Slide 3
Itinerary segmentation strategy development
Clément ALEXANDRE
Internship : 01/02/2021 – 31/07/2021
RAP #2
3

## Slide 4: Summary of the RAP 1 and the tasks carried out since
Analysis of the variation of each parameter
HMI Simulink
Analysis of arithmetic uncertainties
HMI Python
Quadratic uncertainty analysis
Conclusion on the weight of each parameter
RAP 1
Dynamic vehicle model
Dynamic vehicle model
RAP 2
NAVeco presentation

## Slide 5: First approach of uncertainty estimation
Calculation method
Calculation with the extremes of the uncertainty interval for each parameter
Example :
  Parameter a ± Δa
  y1 = ƒ(a-Δa)
  y2 = ƒ(a+Δa)
  [y1; y2] new uncertainty interval
Simulink GUI
NAVeco presentation

## Slide 6: Second approach of uncertainty estimation
Calculation method
Calculation with the derivative
Quadratic uncertainty
Python GUI with PyQt5
Parameters
Results
NAVeco presentation

## Slide 7: Software description : Model Tab
Constants of the dynamic vehicle model
Constants of the dynamic vehicle model
Equation of calculated parameters
To modify the model
NAVeco presentation

## Slide 8: Software description : Parameters Tab
Optimization program which makes it possible to advise an uncertainty as a function of the desired relative uncertainty
Parameters with their uncertainty
Calculated parameters with their calculation methods
Optimization program: advise an uncertainty as a function of the desired relative uncertainty
NAVeco presentation

## Slide 9: Software description : Graph Tab
Optimization program which makes it possible to advise an uncertainty as a function of the desired relative uncertainty
Speed profil
Graph of traction energy, its uncertainty and the desired uncertainty
Numerical results and previous results
NAVeco presentation

## Slide 10: Software description : Uncertainty Tab
Optimization program which makes it possible to advise an uncertainty as a function of the desired relative uncertainty
Uncertainty of the forces and detail of the part of the uncertainty of each parameter
Uncertainty of the traction energy and detail of the part of the uncertainty of each parameter and their weight
NAVeco presentation

## Slide 11: Interest of the software and conclusions on the study
Interest of the software
From which parameters does the uncertainty arise and in which proportion ?
Applicable to any project
How to choose the uncertainty of my sensor ?
Which parameters are most important for route segmentation ?
Conclusion : Weight of each parameter on the uncertainty of the traction energy
Chart: 
| Vitesse | Masse | Pression pneux | Coefs aero | Altitude | Pression air | Température | Pente
 | 0.371 | 0.003 | 0 | 2.686 | 0 | 0 | 0.008 | 96.932
NAVeco presentation

## Slide 12: State of progress
Develop a route segmentation strategy for the NavEco solution
Goal
Intermediate objectives
Application
Means
Study the influence of the parameters on the model
Adapt the vehicle's energy model
Integrate the calculation of uncertainties
Identify important parameters
Retrieve environmental data on the route
Identify the means to recover the data
Route segmentation strategy
Develop a GPS with alternative routes
Adapt the operation of existing GPS
Study of route algorithms
Processed
In progress
Upcoming tasks
Time and distance allocation strategy
Retrieve data
Develop an algorithm
NAVeco presentation

## Slide 13: Real data recovery
Altimetric profile
NAVeco presentation

## Slide 14
Incorporation of electric vehicle specifics in the development of NAVeco
Bastien VENOT
Internship : 01/02/2021 – 31/07/2021
RAP #2

## Slide 15
FORMULATION |  | 
BOLZA |  | 
LAGRANGE | NA | 
 | NA | 
 | NA | 
 | NA | 
FORMULATION |  | 
 | NA | 
 | NA | 
 | NA | 
 | NA | 
Variables  : Distance / : Speed / Power consumption
1st optimization criterion  Power consumption
2nd optimization criterion  Distance OR Speed
1
2
1
2
Search for strategies : Study of optimization problem formulation

## Slide 16
FORMULATION |  | 
BOLZA |  | 
LAGRANGE | NA | 
 | NA | 
 | NA | 
 | NA | 
FORMULATION |  | 
 | NA | 
 | NA | 
 | NA | 
 | NA | 
Search for strategies : Study of optimization problem formulation
Variables  : Distance / : Speed / Power consumption
1st optimization criterion  Power consumption
2nd optimization criterion  Distance OR Speed
1
2
1
2
Discomfort
1
2

## Slide 17
Motor torque (u1)
Torque squared
Torque squared
Cost function formulation
Control criterion expression
Objective
Input variable
CF 1 (Bolza)
CF 2 (Lagrange)
Criteria : Distance, Power, Torque
Criteria : Speed, Power, Torque
Study the sensitivity of factor
Performance indicator
Observation of acceleration profile
Search for strategies : Test for control criteria
Research on the Comfort of Vehicle Passengers Considering the Vehicle Motion State and Passenger Physiological Characteristics
Chang Wang, Xia Zhao, Rui Fu, Zhen Li

## Slide 18
Evolution of the acceleration profile according to the torque penalty factor
Normalization of the criterion in relation to energy AND weigth of importance in the cost function
Exemple of results with quadratic distance error criterion
Distance
Speed
Acceleration
Energy

## Slide 19
Chart: Energy consumption and absolute error of distance according to the factor of control criterion
| 0 | 0,1 | 1 | 10 | 100 | 1000
Energy consumed [Wh] - EQV | 168.11 | 162.76 | 164.73 | 161.12 | 139.71 | 86.26
Energy consumed [Wh] - EQX | 112.52 | 105.95 | 116.51 | 166.96 | 176.84 | 73.83
Abs error of dist [m] - EQV | 0.12 | 0.02 | 0.77 | 8.19 | 76.19 | 349.5
Abs error of dist [m] - EQX | 4.03 | 3.7 | 5.3 | 14.25 | 77.29 | 435.2
Influence of torque penalty on other optimization criteria
1
1
2
EQV : Cost function with quadratic speed error (Lagrange formulation)
EQX : Cost function with quadratic distance error (Bolza formulation)

## Slide 20
Determination of torque penalty factor according to customer requirements
Observation of frequency spectrum
Several low-pass filters with differents cut-off frequencies
Objective : Determine the link between the torque penalty factor and the acceleration frequencies and amplitudes in order to predict the optimal value of Beta according to customer comfort requirements
Results comparison with the curve for Beta=1
Customer requirements (for comfort) :
acceptable acceleration gradient
permissible frequencies in the acceleration profile
Calculation of optimal torque penalty factor
Optimization model
Optimal Beta
Optimal acceleration profile
Solution Diagram
Test methodology

## Slide 21: Status of progress
Integrate the specifics of an electric motor in the development of NAVeco
Objective
Intermediate objectives
Provisions
Means implemented
Study the benefits of regenerative braking
Adapt the energy model of EV
Integrate the regenerative braking feature
Incorporate expression of traction chain performance
Adapt de optimization model
Incorporate the energy model of EV
Study the optimization problem formulation
Study the interest of freewheel strategy and compare with regenerative braking
Adapt the optimization model
Define the slowdown without braking as a criterion to be optimised
Completed
In progress
Futur
Tests for energy and distance optimization
Tests with distance and speed criteria
Tests for comfort optimization
Define the torque criterion
Determination of torque penalty factor according to customer requirements

## Slide 22
Incorporation of thermal engines in the NAVeco development
Hugo DUCHEMANN
Internship : 08/02/2021 – 06/08/2021
RAP #2

## Slide 23: Last RAP : Optimization methods
Présentation NAVeco
Synoptic
Constant acceleration
(limited for each segment)
One-dimensional optimization
Acceleration
Deceleration
Speed limit
Minimum final energy
Iterative algorithm
Dynamic acceleration
Multidimensional optimization
Minimization of the cost function
Taking into accounts the constraints of the dynamic model
Dynamic optimization (MPC or Dynamic programming)

## Slide 24: Optimization methods : Study the impact of different parameters on the compute time
Présentation NAVeco
List of parameters
Objective
Maximum authorized speed on the segment
Initial speed on the segment
The percentage of the slope
The mass of the vehicule
The rolling resistance coefficient
The time to travel the segment
The distance to travel
Determine which algorithm respond best to important varying parameters of the segment
For each value of parameters, 10 measures are made.
Represent the average of the compute time
The dispersion is calculated excluding the extremums
Measures and dispersion
Maximum authorized speed on the segment
Iterative algorithm : Affected
MPC : Affected
Dynamic Programming : Not affected

## Slide 25: Optimization methods : Study the impact of different parameters on the compute time
Method / Parameter | Maximum authorized speed | Initial speed | Percentage of the slope | Mass of the vehicle | Rolling resistant coefficient | Time to travel | Distance to travel
Iterative algorithm | The vehicle arrives or not at his destination -> Increase the compute time | A higher initial speed than the maximum authorized speed decreases the compute time | No effect on compute time | No effect on compute time | No effect on compute time | Increase the computational load | No effect on compute time
Dynamic Programming | No effect on compute time | No effect on compute time | No effect on compute time | No effect on compute time | No effect on compute time | No effect on compute time | No effect on compute time
MPC | The presence of the braking step increase the compute time | No effect on compute time | The percentage of the slope affect the accceleration of the vehicle and the final position -> try to get the vehicle to the final position | The mass affects the acceleration of the vehicle and the final position -> try to get the vehicle to the final position | The coefficient affects the acceleration of the vehicle and the final position -> try to get the vehicle to the final position | Part of an another study | Part of an another study
Présentation NAVeco
Objective
Determine which algorithm respond best to important varying parameters of the segment
25

## Slide 26: Prediction Horizon and Time sample pair study
Présentation NAVeco
Last RAP : Optimization time and final energy of retained binomial
RESULT : For a distance of 1 000 meters and a duration of 60 seconds, we have chosen the pair (6, 2).
Chart: Average time of one optimization and final energy of retained binomials
| 3,8 | 4,1 | 2,9 | 3,7 | 2,7 | 2,1 | 1,8 | 1,9 | 2 | 1,4 | 1,5 | 1,4 | 1,2 | 1,1 | 1 | 1,1 | 0,9 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Final energy | 141.54 | 140.2658 | 140.36 | 140.2658 | 139.42 | 138.26 | 138.57 | 138.2706 | 136.7413 | 141.38 | 139.5813 | 138.84 | 139.89 | 139.48 | 139.4 | 137.3963 | 139.83
Average compute time of one optimization | 0.012002 | 0.012928 | 0.029604 | 0.036018 | 0.061399 | 0.1122 | 0.19089 | 0.19356 | 0.21307 | 0.2662 | 0.27518 | 0.42547 | 0.57595 | 0.77566 | 1.0178 | 1.0964 | 1.2454
Distance errors of (6,2) binomial
Chart: Position error of the (6,2) binomial
| 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 20000 | 30000 | 40000 | 50000 | 60000 | 70000 | 80000 | 90000 | 100000
Total | 8.6468 | 8.7187 | 8.8062 | 8.749 | 8.637 | 8.7296 | 8.7991 | 8.7358 | 8.6323 | 8.7761 | 8.7375 | 8.683 | 8.8049 | 8.6819 | 8.752 | 8.7384 | 8.6375 | 8.8112
The position error does not exceed 9 meters.
Chart: Average time of one optimization and final energy of retained binomials
| 4,8 | 2,9 | 2 | 2,1 | 1,5 | 1,6 | 1,7 | 1,2 | 1,3 | 1,4 | 1,1 | 1,2 | 0,9 | 1 | 0,8 | 0,7 | 0,8 | 0,7 | 0,8 | 0,6 | 0,7 | 0,6 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Final energy | 1073.5864 | 1074.2508 | 1072.8125 | 1071.9132 | 1074.9581 | 1073.971 | 1069.9101 | 1074.0274 | 1072.646 | 1071.9525 | 1073.0245 | 1070.0066 | 1073.2945 | 1071.3972 | 1074.084 | 1074.4374 | 1071.4002 | 1072.0891 | 1068.7182 | 1073.403 | 1069.8088 | 1071.4931
Average compute time of one optimization | 0.0036405 | 0.0062177 | 0.0098912 | 0.0097365 | 0.030273 | 0.033204 | 0.034604 | 0.018359 | 0.019438 | 0.022045 | 0.030929 | 0.036692 | 0.03941 | 0.044056 | 0.052792 | 0.061875 | 0.080219 | 0.087416 | 0.1188 | 0.10446 | 0.16485 | 0.15908
Optimization time and final energy of retained binomial
D =7000m
T = 500s
26

## Slide 27: Prediction Horizon and Time sample pair study
Présentation NAVeco
Test Protocol
Distance : 1 000m to 100 000m (logarithmic scale)
For each distance :
to
(logarithmic scale)
For each time : Test and save every combination of Prediction Horizon and Time sample
Advantages :
Create a database of every binomial and extract the optimal according to permissible position error
Combine 3 tests in a single simulation
Disadvantages :
Very high compute time (193 800 tries)
Number of tries : 19
Number of tries : 17
Number of tries : 600
Example : The duration of the test with a distance of 1 000m, which represent 10 200 tries, was 1 week.
27

## Slide 28: Prediction Horizon and Time sample pair study
Présentation NAVeco
Observation : Time’s impact on energy
Observation : Optimization’s time during optimization
Objective : Reduce the compute time
Complete the vector of speed, position and energy when the vehicle exceeds the desired final position and when the 3 values in the vector are constant
Chart: Final energy of the (6,2) binomial according to the time to travel the segment
| 10 | 20 | 30 | 40 | 43,5 | 50 | 60 | 70 | 80 | 90 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 2000 | 3000 | 3571,4
Total | 30.1464 | 110.361 | 143.9079 | 177.4547 | 179.8212 | 179.8212 | 179.8212 | 179.8345 | 179.8345 | 179.8345 | 179.8345 | 179.8345 | 179.8345 | 179.8345 | 179.8345 | 179.8345 | 179.8345 | 179.8345 | 179.8345 | 179.8345 | 179.8345 | 179.8345
Parameters :
Distance : 1 000m
Time : 60 s
Prediction Horizon : 6*Ts
Time sample : 2s
28

## Slide 29: State of progress
Présentation NAVeco
Traité
En cours
A venir
Notes: (1min30)